## Slide 1: Traffic Model
Xiaoqian Yang
Siyi Xu
Zhaojun Cong

## Slide 2: Assumptions
One road with finite length
One entrance and one exit
Drivers can change the speed according to the traffic condition
Except the speed at entrance and exist should be fixed

## Slide 3: Questions We Want to Focus on
Is there equilibrium of the traffic simplified system ?
Are traffic flows stable?
What’s the relationship between the condition of the whole roadway and the condition on the endpoints?
The maximum capacity under different conditions?

## Slide 4: Extensions We May Refer to:
How does the road condition affect the traffic flow? (weather, traffic bumps )
With multiple lanes on a highway which is more realistic

## Slide 5: Major Variables
Individual vehicle speed (vi): the distance covered per unit time for each vehicle.
The space mean speed (v): v = (n/i=1n1/vi), where n is the number of vehicles passing the roadway segment.
Density (k): the number of vehicles per unit length.
Critical density (kc): the maximum density achievable under free flow.
Jam density (kj): the maximum density achievable under congestion.
Flow Quantity(q): the number of vehicles passing a particular point per unit time. q=kv
Spacing (s): the distance between two vehicles. S=1/k

## Slide 6: Approach Methods
Derive an ODE for each vehicle and analyze the trajectory of the solutions in a time-space diagram.
Derive a PDE for the major variables as functions of time and space. Solve the PDE to get the function of speed, density, quantity, etc. on a roadway.

## Slide 7: Equation 1
The dynamic equation of the car-following model on the single-lane highway can be written as
This defines the acceleration or deceleration of the nth vehicle

## Slide 8: Equation 2
The motion of nth car is given as follows
where xn(t) is the position of the nth vehicle at time t,
∆xn(t) is the headway,
V (∆xn(t)) is the optimal velocity function and τ is the delay time.

## Slide 9: Equation 3
Combine equation 1 and 2

## Slide 10: Equation 4
An extended car-following model by considering the relative velocity is constructed as follows

## Slide 11: Equation 5
The optimal velocity function V(∆xn(t))
where hc is the safety distance
Vmax is the maximal velocity.

## Slide 12: References
Wikipedia: ‘traffic flow’ entry
High way projects that federal administration has.
http://www.fhwa.dot.gov/research/topics/general/
Research on traffic jam problem, this could related to one of our points(Are traffic flows stable? Would it be sensitive to perturbation (e.g. traffic accident at a particular point on the roadway)? )
http://www.scribd.com/nehal0139/d/24861079-Research-on-Traffic-Jam
Yu, L, and Z.-K Shi. "Density Waves in Traffic Flow Model with Relative Velocity." The European Physical Journal B - Condensed Matter. 57.1 (2007): 115-120. Print.